Quinquennial Inspections of Church Buildings in the Diocese

This has been prepared to help Vestries and Property Convenors about Inspection and Reporting to the Vestry and the Diocesan Building Committee about the condition of each Church Building, Hall and any House or Flat in their care. It will help to identify any maintenance requirements and a programme of work to keep those buildings in good repair. Inspections should be budgeted for in the expenditure programme.

Contact with prospective Professional Adviser(s) should be made by phone initially. A Draft follow up Letter of Invitation to the Professional Adviser(s) to submit Fee Proposals for Inspection and Reporting. A Draft Reporting Template is illustrated at the end of this. Electronic copies of the full templates are available from the Diocesan Website.

VESTRY RESPONSIBILITIES

The Province issued guidance about the inspection and report in “Guidance on Quinquennial Building Condition Reports” It appears in full on the SEC website, Vestry Resources, Buildings Section http://www.scotland.anglican.org and a copy can be downloaded’

Briefly, Vestries, with the Rector or Priest in Charge, have a duty to care for the property and fabric of church buildings. The SEC Canons require an inspection and written report every five years (Quinquennial Inspection) on the condition of each building under the Vestry's charge from an inspection carried out by a Chartered Architect or Chartered Surveyor with accreditation in building conservation (see Appendix).

This should ensure early detection of deterioration or defects so that prompt action can be taken, avoiding later and more costly expense, e.g. replacing timbers affected by dry rot. The Report provides a 'snapshot' of the state of the church buildings and shows the extent of the care being given to the building(s). The Vestry can also use it to check on progress made in maintaining property. A Copy of the Report must be provided for the Diocesan Buildings Committee in Perth.

A Vestry can also carry out and record more frequent (eg monthly, annual) inspections of specific items.

The Provincial guidance recommends a Report in the form below. It should be used by the Professional Advisers appointed by a Vestry, although individual Architects or Surveyors may adopt small variations; Vestries should specify the content to be included, and provide the relevant information where necessary (eg in B1, B2, B3, B4, B6 below).

THE REPORT

SECTION A	BACKGROUND

This Section shall identify the Commissioning agent (normally the Vestry), the Letter of Instruction and Appointment of the Inspector, the Report format and list of any previous reports; the Name of the Inspector(s), their Qualifications and Companies, the date(s) of inspection(s), the weather conditions and any other relevant information.

SECTION B – INTRODUCTION

- LIST OF PROPERTIES, with addresses and contact information (phone or fax numbers, or e-mail addresses) for access.

- CUSTODIANS: Rector, Vestry Secretary, Verger & Fabric Convenor with contact details where relevant (phone or fax numbers, or e-mail addresses).

- BRIEF HISTORY OF CONGREGATION: Number on Roll (May be supplemented in Appendix).

- BRIEF DESCRIPTION OF BUILDINGS: Age, Architect (if known), Listing Status etc (May be supplemented in Appendix).

- MATERIALS USED IN THE CONSTRUCTION.

- PREVIOUS MAJOR REPAIRS: Description of Repairs carried out in the last 10 years (from records eg Fabric Record book).

- BRIEF SUMMARY OF CONDITION:

- O.S. PLAN [Current 1:1250 Scale or larger, site centred](The Inspector should be able to provide this)

SECTION C – INSPECTION GUIDELINES (for each building)

Some churches may not have all the elements (eg tower or spire, clock) listed in the following table and some may be inaccessible (eg the Solum - material underneath the floor). Similarly with the building services; the principal ones are the electrical, gas and heating installations. The report need only include those that are present (including any relevant elements not listed in this document).

For ease of reference, the Inspection Report should preferably include a table listing each of the elements of the building with additional information as indicated below.

A EXTERNAL FABRIC:

Roofs:- pitch, materials, flashings, eaves, bargeboards, skews and any chimneys;

Gutters, downpipes and rainwater disposal systems;

Walls, including damp proofing and any under floor ventilation;

Doors and framing, including locks and other fittings, security fittings;

Windows and frames, including any security fittings;

Stained Glass Windows - visual inspection (detailed survey may be required from specialist);

Metalwork and woodwork, including condition of paintwork.

Tower, spire;

Clocks, bells and frames – visual inspection (detailed survey may be required from specialist);

B INTERNAL FABRIC:

Roof structures (eg trusses);

Walls, partitions and ceilings - internal finishes (eg plaster, panelling etc);

Doors and framing, including locks and other fittings, security fittings;

Windows, woodwork and fittings, including any catches for window opening and security fittings;

Internal decorations;

Floors, stairways and balconies;

Solum;

Asbestos – each church should have identified the presence of asbestos and have a management strategy plan.

C FIXTURES AND FITTINGS:

Furniture and fittings - Pews, Pulpit and Font;

Organ - visual inspection (specialist may be required to provide service report);

Monuments (specialist may be required to provide report);

D BUILDING SERVICES:

Lightning conductor - visual inspection (specialist may be required to provide report);

Electrical installation - visual inspection (specialist test/service report), compliance with current Regulations;

Sockets - condition, use of adaptor;.

Lights - type of fitting; use of low energy bulbs;

External Lighting;

Water supply;

Heating system and ventilation – visual inspection (specialist test/service report);

Gas installation – visual inspection (specialist test/service report);

Sound amplification and loop system;

Sanitary facilities and hygiene;

Drainage;

Fire precautions (specialist may be required to provide report);

Security (specialist may be required to provide report).

E GROUNDS:

Including boundaries, paths, trees, notice-boards, etc.

F ACCESS AND PROVISION FOR THE DISABLED:

Comment on provision and options for improvement.

This section of the report should

- list each element of the building;

- briefly describe it;

- assess its condition as excellent, good, acceptable, or poor (with any brief qualification to assist eg sound material, no visible broken or missing xxxxxx) and, where relevant, state compliance with relevant current technical regulations (eg for wiring and switchboard);

- give a brief description of any recommended repairs and their priority - Urgent; Essential or Desirable (ie carry out before the next Quinquennial Inspection), and

- note any regular maintenance required.

SECTION D – SUMMARY

This section should be self-contained and suited to photocopying for general distribution. It should summarise the repair works requiring immediate action, essential within the next twelve months or requiring a specialist report, with a broad outline of the essential and desirable works.

SECTION E – APPENDIX

Additional relevant information to be included here e.g. Listing description, plans, old photographs etc.

________________________________________________________________________________________

APPENDIX A – Other Sources of Information on Quinquennial Inspections.

There are also other sources of information about possible details for inclusion in Quinquennial Inspections of Church buildings, halls, rectories and other properties.

The Scottish Churches Trust ( including involvement of the SEC) has put together guidance on quinquennial inspections and building maintenance (Search under "Maintain your Church" and “Maintenance Articles” on the Scotland's Churches Trust website for their articles on inspection and maintenance. Website http://www.scotlandschurchestrust.org.uk/maintain-your-church):-

The website offers advice, guidance and knowledge on Church maintenance. It offers all denominations access to relevant church building maintenance information and a discussion forum (see sections on “Maintenance Articles”, and “Topic 3: Inspecting your Building Fabric” with brief guidance on routine and cyclical inspections.

The Church of England and some of its dioceses (especially London) have compiled advice and guidance on Quinquennial Inspections with items to be included. In the CoE system inspection of church buildings is by an architect or chartered building surveyor (‘professional advisers') approved by the Diocesan Advisory Committee (DAC). Website http://www.churchcare.co.uk/churches/guidance-advice/looking-after-your-church – see “Looking after your Church” under the Guidance and Advice section for Churches.

The Church of Scotland has produced instructions for the Financial Boards of Congregations about registering, maintaining and inspecting church buildings. Each Board must appoint a Fabric Committee, including or helped by people with technical knowledge and experience in dealing with property. The instructions specify external and internal features that should be inspected annually, their condition recorded and notes made of any work required, plus certain safety inspections. These records are inspected quinquennially by Presbytery.

APPENDIX B – Professional Advisers.

An Architect is a person trained in the planning, design and oversight of the construction of buildings.

A Surveyor (in this context) is a person trained in land, property and construction.

The Royal Incorporation of Architects in Scotland (RIAS) is the professional body for all chartered architects in Scotland. The Royal Institute of British Architects (RIBA) partners with the Royal Incorporation of Architects in Scotland (RIAS). Professionals are Chartered Members of the RIAS or RIBA, usually Member or Fellow. Some have additional qualifications. Those who care for churches may be members of the Ecclesiastical Architects' and Surveyors' Association (EASA): others may also be members of amenity societies, for example the Georgian Group or the Society for the Protection of Ancient Buildings (SPAB). The RIAS offers Accreditation in building conservation which confirms qualification and experience for professionals in conservation work.

The Royal Institution of Chartered Surveyors (RICS) is an independent professional body which regulates property professionals and surveyors in the United Kingdom, and is committed to setting and upholding the highest standards of excellence and integrity. Professionals may be Fellows who may use "FRICS" after their names and Members with "MRICS" after their names.

Draft letter of Invitation to Professional Advisers to submit Fee Proposals for Inspection and Reporting

From the Secretary of the Vestry to one or more Professional Advisers. * delete brackets and any items enclosed [   ] that are not applicable

Dear

QUINQUENNIAL INSPECTION OF CHURCH

(NAME OF CHURCH, DEDICATION AND DIOCESE)

Following a phone call from [insert name, Property Convenor or other designation], the Vestry of (name of church, dedication and diocese) would like to invite [you] / [your company]* to submit your proposed fees for carrying out [a] / [regular]* Quinquennial Inspections as required by the General Synod of the Scottish Episcopal Church and in accordance with the current guidance from the Diocesan Buildings Committee (copy, including a list of the elements of the building attached), [and to advise on, prepare specifications for, and oversee subsequent repairs where invited to do so]*.

Inspection is to be carried out on the following basis:

- The Professional leading the Inspection and preparing the Report is required to have accreditation in building conservation.

- The inspection of the church to be visual and such as can be made from ground level, ladders and any readily accessible roofs, galleries or stagings, and only selected areas will be examined in detail. Parts of the structure which are inaccessible, enclosed or covered will not normally be opened up unless specifically requested. The Vestry shall provide ladders and any other necessary assistance. Any other detailed requirements are to be agreed with the [Property Convenor] / [Vestry Secretary]*.

- The inspection is to include as far as practicable all features of the building, covering all aspects of conservation and repair, and include any ruins and trees within the grounds.

- The report is to be prepared and presented in conformation with the SEC Provincial Scheme and current guidance from the Diocesan Buildings Committee.

- A draft Report is to be submitted within twenty-eight days of carrying out the inspection for any comments by the Vestry. Any comments by the Vestry will be submitted by the Secretary within a further twenty-eight days from receipt of the draft. After that date the report is to be finalised taking account of any comments received from the Vestry Secretary. Four copies of the final report are to be produced; three to be sent to the Vestry Secretary (one for the Rector or Priest in Charge, two for Vestry use) and one to be forwarded to the Secretary of the Diocesan Buildings Committee in Perth. By mutual agreement the report may be produced electronically in both a pdf and one other format.

The fee proposal for the Inspection and Report is to include all costs and provide

- The name(s) and qualifications of the proposed Professional(s); and

- The names of any companies to be used to provide specialist technical assistance (eg testing the electrical installation).

[The fee proposal for advising on, preparing specifications for, and overseeing subsequent repairs should be quoted separately.]*

[Similar invitations are being sent to other Companies and] the appointment will be made on the basis of (i) the lowest fee proposal (ii) the qualifications of the Professional proposed to lead the Inspection and (iii) any other supporting information submitted.

The Vestry accepts that the appointment is likely to be subject to agreement in terms of [the RIAS/RIBA Standard Form of Agreement for the Appointment of an Architect] / [the RlCS Conditions of Engagement for Building Surveying Services]* The appointment as a professional adviser will continue until terminated by either party.

lf there are any issues about the proposed appointment that you wish to discuss, please feel free to contact me with a view to resolving the matter.

Yours Sincerely

[Vestry Secretary / Property Convenor]

* delete brackets and any items enclosed [   ] that are not applicable

Draft Reporting Template

| Element Reference | Element | Description | Condition | Repairs Recommended | Priority U E D | U | Cost E | D |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | EXTERNAL FABRIC |  |  |  |  |  |  |  |
| A1 | Roof | pitch, materials |  |  |  |  |  |  |
|  | flashings |  |  |  |  |  |  |  |
|  | eaves, |  |  |  |  |  |  |  |
|  | skews |  |  |  |  |  |  |  |
| A2 | Gutters |  |  |  |  |  |  |  |
| A3 | Downpipes |  |  |  |  |  |  |  |
| A4 | Walls |  |  |  |  |  |  |  |
|  | INTERNAL FABRIC |  |  |  |  |  |  |  |
|  | FIXTURES AND FITTINGS |  |  |  |  |  |  |  |
|  | BUILDING SERVICES |  |  |  |  |  |  |  |
|  | GROUNDS |  |  |  |  |  |  |  |
|  | ACCESS AND PROVISION FOR THE DISABLED |  |  |  |  |  |  |  |